## Slide 1
Shear Stress
Shear Strain Rate
shear-thickening
shear-thinning
shear-constant

## Slide 2
 |  | Description | Examples | Applications
Shear thinning | pseudoplastic | shear viscosity decreases with applied stress in a time-independent way ( with ) | Ketchup, whipped cream, paint, blood | Commercial products, such as paint, where viscosity is low for application but high once applied
 | thixotropic | shear viscosity decreases over time for a given stress; they thin when shaken | Paints, inks, solder pastes, thread-locking fluid | Fisher Space Pen
Shear thickening | viscoelastic | Acts as a viscous liquid over long time scales but an elastic solid over short ones | Silly Putty, ligaments, tendons | Body armor, toys
 | dilatant | shear viscosity increases with applied stress in a time-independent way ( with ) | oobleck, wet sand, quicksand, silica within polyethylene glycol | Liquid body armor, brake pads, all wheel drive
 | rheopectic | shear viscosity increases over time for a given stress; they thicken when shaken | Gypsum pastes, printer inks, | Body armor, shock absorption
 |  | Description | Examples | Applications
Shear thinning | pseudoplastic |  | Ketchup, whipped cream, paint, blood | Commercial products, such as paint, where viscosity is low for application but high once applied
 | thixotropic | shear viscosity decreases over time for a given stress; they thin when shaken | Paints, inks, solder pastes, thread-locking fluid | Fisher Space Pen
Shear thickening | viscoelastic | Acts as a viscous liquid over long time scales but an elastic solid over short ones | Silly Putty, ligaments, tendons | Body armor, toys
 | dilatant |  | oobleck, wet sand, quicksand, silica within polyethylene glycol | Liquid body armor, brake pads, all wheel drive
 | rheopectic | shear viscosity increases over time for a given stress; they thicken when shaken | Gypsum pastes, printer inks, | Body armor, shock absorption
Shear thickening (systems crystalize under stress)